## Slide 1: CHARGE PUMP DESIGN FOR ULTRA - LOW POWER PLLs
BY: R. F. ADDO
04/26/2011

## Slide 2: OUTLINE
Motivation
Introduction
Design Considerations for PLL’s Charge Pump
  Charge Sharing
  Charge Injection
  Clock Feedthrough
  Current Mismatch
Charge pump Designs
  Design 1: Current Steering NMOS Topology
  Design 2: Current Steering NMOS Topology With Dual Compensation method
  Design 3: NMOS Topology With No Current Steering
  Design 4: Novel Design
Simulation Results Summary and Conclusion
Reference
Questions

## Slide 3: MOTIVATION
The need for ultra – low power PLL has increased.
Depending on the type of VCO used, the charge pump contribute between 20 % to 50% of the total power consumption of the PLL
Reducing this power consumption will lead to a reduction of the overall power consumed by the PLL

## Slide 4: INTRODUCTION
Charge pump is used to sink and source current into a loop – filter based on the output of a PFD
Issues associated with charge pump are current mismatch, charge sharing, charge injection, noise and high power dissipation
Fig. 1: Block diagram of a typical PLL

## Slide 5: INTRODUCTION (CONT.)
UP state: the switch SM1 is on and
SM2 is off
Fig. 2a: Schematic of conventional charge pump [5]
Fig. 2b: Output waveform of a typical charge pump: Pumping Up

## Slide 6
INTRODUCTION (CONT.)
DOWN state: SM1 is off and SM2 is
on
Fig. 3a: Schematic of conventional charge pump [5]
Fig. 3b: Output waveform of a typical charge pump: Pumping Down

## Slide 7
HOLD state: SM1 and SM2 are both off, then no current flows into CL and Vc is held, which means that the PLL is locked.
In ideal case, SM1 and SM2 will never be on at the same time.
INTRODUCTION (CONT.)
Fig. 3c: Output waveform of a typical charge pump when the PLL is locked

## Slide 8: Design Considerations For PLL’s Charge Pump
The necessary requirements for designing an effective charge pump circuit are:
  Avoid the charge sharing;
  Minimize the effect caused by charge injection and clock feed-through phenomena
  Match the current values of Iup and Idn and make sure that there is no time mismatch between UP and DN.
  Low power consumption

## Slide 9: Charge Sharing
This depends on the position of the
There exists a short time when the UP and DOWN
Signals are all one
This will cause the voltage at node X to decrease
and that at node Y to increase which will cause a
deviation in the output voltage
This will lead to reference spurs
[5]
Fig. 4c: Schematic of conventional charge pump with a unity gain amplifier [5]
Fig. 4: Output waveforms, (a) ideal and (b) various non-ideal case [5].
(b)

## Slide 10: Charge Injection
When the current source/sink switches (eg. SM2) are on, there are charges under the gate of the transistor.
When the switch is turned off, the charge under the gate will be injected to the drain (node Vc) and the source (node Y) of the transistor and cause ripple at the output as shown in curve III of fig.
Fig. 5a: Schematic of conventional charge pump with a unity gain amplifier [5]
Fig. 5b: Output waveforms, various non-ideal cases [5].

## Slide 11: Clock Feedthrough
This is due to the coupling capacitance from the gate to both the source and drain of the CMOS device as shown in fig 6a.
Whenever the clock goes low, a capacitive voltage divider between the gate/drain and CL
This will also cause ripple at the output as in curve IV
Fig. 6b: Output waveforms, various non-ideal cases [5].
Fig. 6a: Clock Feedthrough
CL
Vout

## Slide 12: Charge Injection and Clock Feedthrough Reduction
Dummy Switch
A dummy switch as shown in fig 7 which
is a MOS device with its drain and source
shorted and placed in series with the
desired switch M1 with its control signal
being the inverted signal of that of M1.
Transmission Gate
A transmission gate with complementary signal at its input which will act to cancel each other out however a precise control of the complementary signals used is required (i.e. they must be switched exactly at the same time)
Fig. 7: Using dummy switch to reduce the charge injection and the clock feedthrough effects in a charge pump
M1
M2

## Slide 13: Current Mismatch
Mismatch between lup and Idn or delay between UP and DN signals leads to a nature phase error even when the PLL is locked
Qcharge = lup x tup = Qdischarge = ldn x tdn
[5]
Fig. 8: Mismatch issue in charge pump circuits.[5]

## Slide 14: Current Mismatch Minimization
  The current mismatch can be reduced by either increasing the output resistance of the pump or to use a compensation method
  Increasing the Output Resistance
  using a cascode or a gain – boosting topology to attain this.
  Compensation Method
  Operational amplifier is used to enable Iup and Idn track each other.
Fig. 9a: Schematic of conventional cascode charge pump [2]
Fig. 9c: Schematic of conventional compensated charge pump [2]

## Slide 15: OUTLINE
Motivation
Introduction
Design Considerations for PLL’s Charge Pump
  Charge Sharing
  Charge Injection
  Clock Feedthrough
  Current Mismatch
Charge pump Designs
  Design 1: Current Steering NMOS Topology
  Design 2: Current Steering NMOS Topology With Dual Compensation method
  Design 3: NMOS Topology With No Current Steering
  Design 4: Novel Design
Simulation Results Summary and Conclusion
Reference
Questions

## Slide 16: Design 1:Charge Pump Without Compensation Method [4]
This design utilizes current steering switches to implement an NMOS topology charge pump
Fig.10: Schematic of the NMOS charge pump without compensation

## Slide 17: Design 1: Charge Pump Without Compensation Method [4] Results
VDD (V) | POWER @ 1GHz | CURRENT MISMATCH (%) | PHASE NOISE (dBc/Hz) @ 1MHz OFFSET
0.7 | 19.13µW | 1.872 | -104.3
Fig.11: Phase noise of the NMOS charge pump without compensation

## Slide 18: Design 2: Charge Pump With Dual Compensation Method [4]
To minimize the current mismatch, two differential amplifiers are used
This gives an improvement in the current mismatch at the expense of power
Fig.12: Schematic of the NMOS charge pump with compensation
VR
VR

## Slide 19: Design 2: Charge Pump With Dual Compensation Method (Cont)
Fig. 13a: Schematic of the differential amplifier with NMOS input devices (N)
Fig. 13b: Schematic of the differential amplifier with PMOS input devices (P)

## Slide 20: Design 2: Charge Pump With Dual Compensation Method [4] Result
VDD (V) | POWER @ 1GHz | CURRENT MISMATCH (%) | PHASE NOISE (dBc/Hz) @ 1MHz OFFSET
0.7 | 34.42µW | 0.889 | -101.83
Fig. 14: Phase noise of the NMOS charge pump with compensation

## Slide 21: Design 3: NMOS Topology Charge Pump [15]
This implements an NMOS topology charge pump
The difference between this design and that of designs 1 and 2 is that it does not use any current steering switches
It attains relatively good phase noise
Fig. 15: Schematic of the NMOS charge pump topology

## Slide 22: NMOS Topology Charge Pump [15] Result
VDD (V) | POWER @ 1GHz | CURRENT MISMATCH (%) | PHASE NOISE (dBc/Hz) @ 1MHz OFFSET
0.7 | 18.89µW | -4.68 | -104.35
Fig. 16: Phase noise of the NMOS charge pump topology

## Slide 23: Novel Charge Pump
The PMOS used for the current mirror in a typical NMOS topology charge pump has been replaced with NMOS devices
This design attained the lowest power compared with the previous three designs
Fig. 17: Schematic of the novel NMOS only charge pump

## Slide 24: Novel Charge Pump Result
VDD (V) | POWER @ 1GHz | CURRENT MISMATCH (%) | PHASE NOISE (dBc/Hz) @ 1MHz OFFSET
0.7 | 288.4nW | 4.25 | -84.91
Fig. 18: Phase noise of the novel NMOS only charge pump

## Slide 25: Result Summary
Result summary
DESIGN | VDD (V) | POWER @ 1GHz | CURRENT MISMATCH (%) | PHASE NOISE (dBc/Hz) @ 1MHz OFFSET
1 | 0.7 | 19.13µW | 1.872 | -104.3
2 | 0.7 | 34.42µW | 0.889 | -101.83
3 | 0.7 | 18.89µW | -4.68 | -104.35
THIS WORK | 0.7 | 288.4nW | 4.25 | -84.91
OTHER WORKS |  |  |  | 
REFERENCE | PROCESS TECHNOLOGY | VDD (V) | REFERENCE FREQUENCY (MHz) | PHASE NOISE (dBc/Hz)
[16] | 0.35µm | 2 | 40 (50) | -86 @ 10kHz Offset
[17] | 0.25µm | 1.5 | 43 | -75 @ 40kHz Offset
[18] | 0.25µm | 2.5 | 10 | -63 @ 10kHz Offset
[19] | 0.25µm | 2.5 | 4 | -77 @ 10kHz Offset
[20] | 0.18µm | 1.8 | 20 | -79 @ 10kHz Offset
[21] | 0.18µm | 1.8 | 12.5 | -90 @ 1kHz Offset

## Slide 26: Conclusion
For ultra – low power Charge Pump PLL design, with moderate phase noise requirement, the novel charge pump design presented in this work could be used
This design could further be improve so that the current mismatch and the phase noise could be lowered and be able to operate at lower voltage

## Slide 27: Reference
[1] Woogeun Rhee, “Design of High – Performance CMOS Charge Pumps in Phase – locked loops.”
[2] Dong – Keon Lee, Jeong – Kwang Lee, and Hang – Geun Jeong, “A Dual – Compensated Charge Pump with Reduced Current Mismatch”
[3] M.-S. Hwang, J. Kim and D.-K. Jeong, “Reduction of pump current mismatch in charge-pump PLL” http://ieeexplore.ieee.org/stamp/stamp.jsp?tp=&arnumber=4770439
[4] Jae Hyung Noh, and Hang Geun Jeong, “Charge-Pump with a Regulated Cascode Circuit for Reducing Current Mismatch in PLLs”
[5] Hong Yut, Yasuaki Inouet, and Yan Han, “A New High-Speed Low-Voltage Charge Pump for PLL Applications” http://ieeexplore.ieee.org/stamp/stamp.jsp?tp=&arnumber=1611344
[6] Kyung-Soo Ha and Lee-Sup Kim, “Charge-Pump reducing current mismatch in DLLs and PLLs” http://ieeexplore.ieee.org/stamp/stamp.jsp?tp=&arnumber=1693061
[7] Shanfeng Cheng, Haitao Tong, Jose Silva-Martinez, and Aydin Ilker Karsilayan, “Design and Analysis of an Ultrahigh-Speed Glitch-Free Fully Differential Charge Pump With Minimum Output Current Variation and Accurate Matching”

## Slide 28: Reference (Cont.)
[8] Jean-François Richard and Yvon Savaria, “High Voltage Charge Pump Using Standard CMOS Technology”
[9] Janusz A. Starzyk, Ying-Wei Jan, and Fengjing Qiu, “A DC–DC Charge Pump Design Based on Voltage Doublers”
[10] Nick Van Helleputte and Georges Gielen “An Ultra-low-Power Quadrature PLL in 130nm CMOS for Impulse Radio Receivers” http://ieeexplore.ieee.org/stamp/stamp.jsp?tp=&arnumber=4463309&tag=1
[11] Q. Guo, H. F. Zhou, W. W. Cheng, Y. Han, X. X. Han, and X. Liang, “A Low Phase-noise Low-power PLL in 0.13-¹m CMOS for Low Voltage Application”
[12] Gong Zhichao, Lu Lei, Liao Youchun, and Tang Zhangwen, “Design and noise analysis of a fully-differential charge pump for phase-locked loops”
[13] Po-Yao Ke and Jon Guerber, “A 1.3V Low Power Divide by 4 PLL Design with Output Range 0.5GHz-1.5 GHz”
[14] Partha Pratim Ghosh, “ Design and Study of Phase Locked Loop for Space Applications In Submicron CMOS Technology”
[15] Tsan – Huei Wu, “ Low – Cost Jitter Measurement Techniques for Phase Locked Loops.”
[16] Keliu Shu, Edgar Sanchez – Sinencio, Jose Silva – Martinez, and Sherif H. K. Embabi, “A 2.4 – GHz monolithic fractional – N frequency synthesizer with robust phase – switching prescaler and loop capacitance multiplier”

## Slide 29: Reference (Cont.)
[17] C. M. Hung and K. K. O, “A fully integrated 1.5 – V 5.5 – GHz CMOS phase – locked loop”
[18] S. Pellerano, S. Laventino, C. Samori, and A. Lacaita, “A 13.5 – mW 5-GHz frequency synthesizer with dynamic – logic frequency divider”
[19] F. Herzel, G. Fischer, and P. Weger, “An integrated CMOS RF synthesizer for 802.11a wireless LAN”
[20] Chun – Yi Kuo, Jung – Yu Chang, and Shen – Iuan Lui, “A spur – reduction technique for a 5 – GHz frequency synthesizer”
[21] A fully differential charge pump with accurate current matching and rail – to – rail common – mode feedback circuit.”
BOOKS:
    Low – Voltage CMOS RF Frequency Synthesizers by Howard C. Luong and Gerry C. T. Leung
    High Speed CMOS Circuits for Optical Receivers by Jafar Savoj and Behzad Razavi
    PLL Performance, Simulation and Design by Dean Banerjee

## Slide 30
QUESTIONS